## Slide 1: MOTORCYCLE SAFETY SYSTEM

## Slide 3
ESP32 SIM800L Module
Helmet with MQ3 sensor
App Access Sensor Data
Send data to cloud platform, ThingsBoard
Send message automatically to authorized contact when detect accident
Motorcycle equipped with multiple sensors and camera
LM35
Neo 6M GPS
MPU6050
HC - SR04
ESP32-CAM
Termination
button
Push Button
MQ3 Sensor

## Slide 4: System States
Ignition State / Operational State
Ultrasonic Sensor ,HC- SR04
ESP32 Cam
Neo 6M GPS Module
Components that are active in this state:
MQ3
LM35
MPU6050
Parking State / Non-Operational State
Components that are active in this state:
Ultrasonic Sensor ,HC- SR04
ESP32 Cam
Neo 6M GPS Module

## Slide 5
Start
Connect to the GSM/GPRS module (ESP32 SIM800L)
Check for helmet and alcohol presence
Helmet?
Alcohol ?
Send an alert message to pre- specified number
Provide permission to start the motorcycle
System continuously monitors alcohol level, engine temperature, speed, lean angle, distance with other vehicle and location as well as sends data to cloud
> threshold value?
Accident?
Send GPS location to emergency contact via SMS
Terminate
yes
no
no
yes
yes
ESP32 Cam checks for authorized user
no
yes
no
yes
[Abort sending message]

## Slide 8
YOLO Tiny V3
Load the model into the browser
Person Detection
Face Recognition

## Slide 10
Start
Connect to the GSM/GPRS module (ESP32 SIM800L)
Continuously monitors nearby distance via ultrasonic sensor
Distance with nearby object < threshold ?
ESP32 Cam triggered, capture the front view and send it to the pre-specified mail address
ESP32 CAM scan for intruder face
Neo 6M GPS module activate
Continue the alert state?
Terminate
yes
no
yes
no

## Slide 11
Deep Sleep
Nearby Object Detected
Person Detected
Capture Image
Save Image to SD Card
Mail the Image

## Slide 13: ThingsBoard Dashboard

## Slide 19: Alert Messages

## Slide 20
Total acceleration
Lateral acceleration
Acceleration due to
gravity, g

## Slide 22
z-axis
x-axis
y-axis
Pitch
Roll
Yaw
+
-
+
-
+
-

## Slide 26
ESP32 SIM800L
MQ3 Sensor
Push Button
X 2
LM35
HC-SR04
Ultrasonic Sensor
X 3
Servo Motor
X 3
Neo 6M GPS
Module
ESP32 CAM
MPU6050
ADS1115 16-Bit
Buzzer
LED Indicators
X 3
Power Supply

## Slide 30
Object
distance 40 cm
< 90cm
distance 125 cm
> 90cm

## Slide 31
Accident happened
Emergency contact receive
the message and location
Alert message is sent to the emergency contact by ESP32 SIM800L
GPS module traces
the location
Emergency services
receive the call
Ambulance for medical assistance
Patient is being shifted to hospital

## Slide 32
Conv 3*3 416*416*16
Maxpool 2*2 208*208*16
Conv 3*3 104*104*64
Conv 1*1
Conv 1*1 13*13*128
Upsample 26*26*384
Concat 26*26*384
Conv 3*3 26*26*256
Conv 1*1
Conv 3*3 52*52*128
Conv 3*3 208*208*32
Conv 3*3 13*13*1024
Conv 3*3 26*26*256
Conv 1*1 13*13*256
Conv 3*3 13*13*512
Conv 3*3 13*13*512
Maxpool 2*2 13*13*256
Maxpool 2*2 52*52*64
Maxpool 2*2 104*104*32
Maxpool 2*2 26*26*128
Maxpool 2*2 13*13*512
Output 1
13*13*255
Input
416*416*3
Output 2
26*26*255

## Slide 34
ThingsBoard
Sensors Embedded
Vehicle
PC/Laptop
Smartphone
Publisher
MQTT Broker
Subscriber
Subscriber
Publish MQTT Message
MQTT Topic: devices/id/data
Subscribe to MQTT Topic
Subscribe to MQTT Topic
Publish MQTT Data
Publish MQTT Data

## Slide 37
Let's now define the most basic terms, which are whole numbers (not rates):
true positives (TP): These are cases in which we predicted yes (they have the disease), and they do have the disease.
true negatives (TN): We predicted no, and they don't have the disease.
false positives (FP): We predicted yes, but they don't actually have the disease. (Also known as a "Type I error.")
false negatives (FN): We predicted no, but they actually do have the disease. (Also known as a "Type II error.")

## Slide 38
 | Positive | Negative | 
Positive | True Positive (TP) | False Negative (FN) | Recall
Negative | False Positive (FP) | True Negative (TN) | 
 | Precision |  | Accuracy
 | Positive | Negative | 
Positive | True Positive (TP) | False Negative (FN) | 
Negative | False Positive (FP) | True Negative (TN) | 

## Slide 42
Internet of
Things

## Slide 43
Smart Retail
IoT sensors can leverage data from online and in-store sales to drive warehouse automation and robotics. RFIDs, which are already widely used around the world, are used for this.
Healthcare
IoT enabled devices have made remote monitoring in the healthcare sector possible, unleashing the potential to keep patients safe and healthy, and empowering physicians to deliver superlative care.
Wearables
Fitbits, iPhones, Apple watches, and health monitors, to mention a few, are examples of wearables. These devices increase entertainment, network connectivity, health, and fitness.
Smart Agriculture
IoT-enabled devices can detect soil moisture and nutrients, as well as weather data, to improve the control of smart irrigation and fertilizer systems.
Transportation
IoT is projected to disrupt transportation by lowering delays, forecasting inbound material shortages, and modifying orders in the middle of manufacturing based on real-time demand data.
Smart Homes and Cities
IoT significantly improves the way we control and monitor all the processes taking place at our home. IoT devices such as linked sensors, lighting, and meters are used in smart cities to gather and analyze data which are then used by cities to enhance infrastructure, public utilities, and services, among other things.
IOT
Notes: © Copyright PresentationGO.com – The free PowerPoint and Google Slides template library

## Slide 45
YEAR-WISE ROAD CRASHES AND DEATH |  | 
YEAR | ACCIDENTS | DEATH
2020 | 4891 | 6686
2019 | 5516 | 7855
2018 | 5514 | 7221
2017 | 4979 | 7397
2016 | 4317 | 6055

## Slide 46
Chart: Vehicles Involved in accidents
| Battery-run easy bike | Car,microbus | Autorickshaw | Bus | Tractor,locally made vehicles | Truck,lorry,covered van | Motorcycle
Accident Involvment (percentage) | 8.04 | 5.22 | 9.35 | 18.99 | 7.32 | 29.82 | 21.4
YEAR-WISE ROAD CRASHES AND DEATH |  | 
YEAR | ACCIDENTS | DEATH
2020 | 4891 | 6686
2019 | 5516 | 7855
2018 | 5514 | 7221
2017 | 4979 | 7397
2016 | 4317 | 6055

## Slide 49
Applications
Application Layer
Processing Unit
Data Processing Layer
Gateways
Network Layer
Sensors
Sensing Layer

## Slide 53
MatMul
Add
Relu
w
x
b
User Fetches
Outputs
TensorFlow
Flows Tensors
TensorFlow
Trains
Variables
User Feeds
Inputs
TensorFlow Performs
Operations

## Slide 55
Service | Availability
Vital Registration System | Yes
Emergency Room Based Injury Surveillance System | No
Emergency Access Telephone Numbers | Yes
Seriously Injured Transported by Ambulance | ≤ 10%
Permanently disabled due to Road traffic Crash | 220 people everyday

## Slide 57
Manuscripts identified through google scholar searching
(n = 127 )
Additional manuscripts identified through other sources
(n= 19)
Manuscripts after duplicates removed
(n= 114)
Full-text articles assessed for eligibility
( n= 69)
Studies included for literature review
( n= 52 )
Full-text manuscripts excluded because of unclear explanation, not focus on vehicle safety and security
(n= 16)
Identification
Screening
Eligibility
Included
Manuscripts excluded on the basis of titles, abstract and journal because they did not focus on accident detection or prediction
(n= 45 )

## Slide 65
YOLO was created to help improve the speed of slower two-stage object detectors, such as Faster R-CNN.
While R-CNNs are accurate they are quite slow, even when running on a GPU.
On the contrary, single-stage detectors such as YOLO are quite fast, obtaining super real-time performance on a GPU.
The downside, of course, is that YOLO tends to be less accurate (and in my experience, much harder to train than SSDs or RetinaNet).
Since Tiny-YOLO is a smaller version than its big brothers, this also means that Tiny-YOLO is unfortunately even less accurate.
For reference, Redmon et al. report ~51-57% mAP for YOLO on the COCO benchmark dataset while Tiny-YOLO is only 23.7% mAP — less than half of the accuracy of its bigger brothers.
That said, 23% mAP is still reasonable enough for some applications.
My general advice when using YOLO is to “simply give it a try”:
In some cases, it may work perfectly fine for your project.
And in others, you may seek more accurate detectors (Faster R-CNN, SSDs, RetinaNet, etc.).
https://www.pyimagesearch.com/2020/01/27/yolo-and-tiny-yolo-object-detection-on-the-raspberry-pi-and-movidius-ncs/